| 7/16 DIN Female 35mm SQ Mount Connector For RG401(250In) Cable Interface |
| --- |
| According to | IEC 60169-4 |
| Electrical |  |
| Characteristic Impedance | 50 ohm |
| Frequency Range | DC-7.5GHz |
| VSWR | ≤1.10@DC-3000MHz |
| Dielectric Withstanding Voltage | ≥4000V RMS,50Hz,at sea level |
| Dielectric Resistance | ≥10000MΩ |
| Contact Resistance | Center Contact ≤0.4mΩ |
|  | Outer Contact ≤1 mΩ |
| Intermodulation 3rd (PIM3) | ≤ -155dBc@2�20W |
| Mechanical |  |
| Durability | Mating cycles ≥500 |
| Material and plating |  |
|  | Material | Plating |
| Body | Brass | Tri-Metal |
| Insulator | PTFE(Teflon) | － |
| Center conductor | Phosphor Copper | Ag |
| Gasket | Silicone Rubber | － |
| Environmental |  |
| Temperature Range | -40℃～+85℃ |
| Weatherproof Rate | IP 68 |
| RoHs Compliant |  |
| Interface |
| According to | IEC 60169-4 |
| Electrical |  |
| Characteristic Impedance | 50 ohm |
| Frequency Range | DC-7.5GHz |
| VSWR | ≤1.10@DC-3000MHz |
| Dielectric Withstanding Voltage | ≥4000V RMS,50Hz,at sea level |
| Dielectric Resistance | ≥10000MΩ |
| Contact Resistance | Center Contact ≤0.4mΩ |
|  | Outer Contact ≤1 mΩ |
| Intermodulation 3rd (PIM3) | ≤ -155dBc@2�20W |
| Mechanical |  |
| Durability | Mating cycles ≥500 |
| Material and plating |  |
|  | Material | Plating |
| Body | Brass | Tri-Metal |
| Insulator | PTFE(Teflon) | － |
| Center conductor | Phosphor Copper | Ag |
| Gasket | Silicone Rubber | － |
| Environmental |  |
| Temperature Range | -40℃～+85℃ |
| Weatherproof Rate | IP 68 |
| RoHs Compliant |  |