7/16 DIN Female Connector For 7/8� Foam Feeder Cable

Interface

According to                                               IEC 60169-4

Electrical

Characteristic Impedance                                      50 ohm

Frequency Range                                            DC-7.5GHz

VSWR                                                  ≤1.12@DC-3000MHz

Dielectric Withstanding Voltage                     ≥4000V RMS,50Hz,at sea level

Dielectric Resistance                                          ≥10000MΩ

Contact Resistance                                     Center Contact ≤0.4mΩ

Outer Contact ≤1 mΩ

Mechanical

Durability                                           Mating cycles  ≥500

Material and plating

Material                   Plating

Body                        Brass                              Ni

Insulator                     PTFE                            －

Center conductor              Phosphor bronze                          Ag

Coupling Nut                 Brass                                     Ni

Other Parts                   Brass                                     Ni

Gasket                      Silicone Rubber                             －

Environmental

Temperature Range                                             -40℃～+85℃

Weatherproof Rate                                                   IP 68

RoHs Compliant