7/16 DIN Male Connector for 7/8� Foam Feeder Cable

Interface

According to                                               IEC 60169-4

Electrical

Characteristic Impedance                                      50 ohm

Frequency Range                                            DC-7.5GHz

VSWR                                                ≤1.10@DC-3000MHz

Dielectric Withstanding Voltage                      ≥4000V RMS,50Hz,at sea level

Dielectric Resistance                                          ≥10000MΩ

Contact Resistance                                     Center Contact ≤0.4mΩ

Outer Contact ≤1 mΩ

Mechanical

Durability                                           Mating cycles  ≥500

Material and plating

Material                 Plating

Body                        Brass                           Ni

Insulator                     PTFE                         －

Center conductor              Phosphor bronze                       Ag

Coupling Nut                 Brass                                  Ni

Other Parts                   Brass                                  Ni

Gasket                      Silicone Rubber                          －

Environmental

Temperature Range                                             -40℃～+85℃

Weatherproof Rate                                                   IP 68

RoHs Compliant