1-5/8″EIA Flange Right Angle Connector For 1-5/8″Foam Feeder Cable

Interface

According to                                          1-5/8In EIA Flange

Electrical

Characteristic Impedance                                      50 ohm

Operating Frequency Range                                     DC-3GHz

VSWR                                                   ≤1.15 @DC-1000MHz

Dielectric Withstanding Voltage          ≥6000V RMS,50Hz,at sea level

Dielectric Resistance                                         ≥5000MΩ

Average Power                                             3.4 KW@900MHz

Peak Power Maximum                                              90KW

Contact Resistance                             Center Contact  ≤1.5mΩ

Outer Contact   ≤1.5mΩ

Mechanical

Durability                                         Mating cycles ≥500

Material and plating

Material             Plating

Body                        Brass                        Ni

Insulator                     PTFE                      －

Center conductor              Phosphor bronze                    Ag

Coupling Nut                 Brass                              Ni

Other Parts                   Brass                              Ni

Gasket                       Silicone Rubber                     －

Bolts and Washer              Stainless Steel                       －

Environmental

Operating Temperature Range                                -45℃～+85℃

Weatherproof Rate                                               IP 67

RoHs Compliant