7/8″EIA Flange Right Angle Connector For 7/8″Foam Feeder Cable

Interface

According to                                            7/8In EIA Flange

Electrical

Characteristic Impedance                                   50 ohm

Operating Frequency Range                                 DC-5GHz

VSWR                                            ≤1.15@DC-1000MHz

Dielectric Withstanding Voltage                  ≥6000V RMS,50Hz,at sea level

Dielectric Resistance                                       ≥5000MΩ

Average Power                                        2.3KW@900MHz

Peak Power Maximum                                          90KW

Contact Resistance                                Center Contact  ≤1.5mΩ

Outer Contact   ≤1.5mΩ

Mechanical

Durability                                          Mating cycles ≥500

Material and plating

Material                            Plating

Body                        Brass                               Ni

Insulator                     PTFE                               －

Center conductor              Phosphor bronze                    Ag

Coupling Nut                 Brass                               Ni

Other Parts                   Brass                               Ni

Gasket                      Silicone Rubber                      －

Bolts and Washer              Stainless Steel                      －

Environmental

Temperature Range                                        -40℃～+85℃

Weatherproof Rate                                               IP 67

RoHs Compliant