Discharge Tube Type Surge Arrester

N Female to N Female Bulkhead

Interface                                               According to IEC 60169-16

Electrical

Characteristic Impedance                                        50 ohm

Dielectric Resistance                                           ≥5000 M ohm

Contact Resistance                                      Center Contact ≤1mΩ

Outer Contact ≤1mΩ

AC Withstand Voltage                 2500V / 1 Min No breakdown and No Arcing Phenomenon

Frequency Range                                                DC-3GHz

VSWR                                                          ≤1.20

Insertion Loss                                                    ≤0.3dB

Initial Discharge Voltage                                    75/90/150/230/350V

Average RF Power                                     30W-400W(Depending on gas tube)

Peak RF Power                                                   ＜600W

Maximum Discharge Current                                     20KA(8/20μs)

Material and Plating

Parts Name                   Material                              Plating

Housing(Body)                 Brass                                  Ni

Insulator                       PTFE                                 －

Center Pin                     Phosphor Bronze                       Au

Inner Conductor                Phosphor Bronze                       Au

O-ring (Sealing)                Silicon Rubber                          －

Standard Component            Stainless Steel                         －

Environmental

Temperature Range                                            -45℃～+85℃

Weatherproof Rate                                                  IP 67

RoHs Compliant