Discharge Tube Type Surge Arrester SMA Male to SMA Female Port

Electrical

Characteristic Impedance                                        50 ohm

Dielectric Resistance                                           ≥5000 M ohm

Contact Resistance                                      Center Contact ≤3mΩ

Outer Contact ≤2.5mΩ

AC Withstand Voltage                   100V / 1 Min No breakdown and No Arcing Phenomenon

Frequency Range                                                DC-3GHz

VSWR                                                          ≤1.15

Insertion Loss                                                    ≤0.18dB

Initial Discharge Voltage                                  75/90/150/230/350V

Average RF Power                                     30W-400W(Depending on gas tube)

Peak RF Power                                                   ＜500W

Maximum Discharge Current                                     20KA(8/20μs)

Material and Plating

Parts Name                    Material                            Plating

Housing(Body)                 Brass                                Ni

Insulator                      PTFE                                －

Center Pin                     Phosphor Bronze                      Au

Inner Conductor                Phosphor Bronze                       Au

O-ring (Sealing)                Silicon Rubber                         －

Standard Component            Stainless Steel                          －

Environmental

Temperature Range                                            -45℃～+85℃

Weatherproof Rate                                                  IP 67

RoHs Compliant