Discharge Tube Type Surge Arrester

N Male to N Female

Interface                                                According to IEC 60169-16

Electrical

Characteristic Impedance                                        50 ohm

Dielectric Resistance                                           ≥5000 M ohm

Contact Resistance                                       Center Contact ≤1mΩ

Outer Contact ≤1mΩ

AC Withstand Voltage                 2500V / 1 Min No breakdown and No Arcing Phenomenon

Frequency Range                                                 DC-6GHz

VSWR                                                     ≤1.15@DC-6GHz

Insertion Loss                                                   ≤0.15dB

Initial Discharge Voltage                                   75/90/150/230/350V

Average RF Power                                     30W-400W(Depending on gas tube)

Peak RF Power                                                  ＜600W

Maximum Discharge Current                                    20KA(8/20μs)

Material and Plating

Parts Name                   Material                            Plating

Housing(Body)                 Brass                                 Ni

Insulator                       PTFE                                 －

Center Pin                     Phosphor Bronze                      Au

Inner Conductor                Phosphor Bronze                       Au

O-ring (Sealing)                Silicon Rubber                         －

Standard Component            Stainless Steel                         －

Environmental

Temperature Range                                             -45℃～+85℃

Weatherproof Rate                                                  IP 67

RoHs Compliant