SMB Jack (Female) Straight Connector For PCB Mount Interface According to IEC 60169-10 CECC 22130 Electrical Characteristic Impedance Frequency Range VSWR Dielectric Withstanding Voltage Dielectric Resistance Contact Resistance 50ohm DC-4GHz ≤1.2@DC-3GHz ≥1000V RMS,50Hz,at sea level ≥1000MΩ Center Contact≤6mΩ Outer Contact≤1mΩ Mechanical Durability Mating cycles≥500 Material and plating Body Insulator Female Contact Material Brass PTFE Phosphor Copper Plating Au - Au Environmental Temperature Range －40℃～＋125℃ Drafted by: Approved by: