SMC Female Right Angle Crimp Connector For RG58 Cable

| Interface |
| --- |
| According to | IEC 60169-9；CECC22140；DIN47225 |
| Electrical |  |
| Characteristic Impedance | 50 ohm |
| Typical Frequency Range | DC-6GHz |
| VSWR | ≤1.25@DC-3GHz |
| Dielectric Withstanding Voltage | ≥1000V RMS,50Hz,at sea level |
| Dielectric Resistance | ≥5000MΩ |
| Contact Resistance | Center Contact ≤6mΩ |
|  | Outer Contact ≤2.5mΩ |
| Mechanical |  |
| Durability | Mating Cycles ≥500 |
| Material and Plating |  |
|  | Material | Plating |
| Body | Brass | Au |
| Insulator | PTFE(Teflon) | － |
| Center conductor | Phosphor Copper | Au |
| Resilient Contact | Phosphor bronze | Au |
| Ferrule | Annealed Copper | Ni |
| Gasket(O-ring) | Silicone Rubber | － |
| Environmental |  |
| Operating Temperature Range | -40℃～+85℃ |
| RoHs | Compliant |  |
| Interface |
| According to | IEC 60169-9；CECC22140；DIN47225 |
| Electrical |  |
| Characteristic Impedance | 50 ohm |
| Typical Frequency Range | DC-6GHz |
| VSWR | ≤1.25@DC-3GHz |
| Dielectric Withstanding Voltage | ≥1000V RMS,50Hz,at sea level |
| Dielectric Resistance | ≥5000MΩ |
| Contact Resistance | Center Contact ≤6mΩ |
|  | Outer Contact ≤2.5mΩ |
| Mechanical |  |
| Durability | Mating Cycles ≥500 |
| Material and Plating |  |
|  | Material | Plating |
| Body | Brass | Au |
| Insulator | PTFE(Teflon) | － |
| Center conductor | Phosphor Copper | Au |
| Resilient Contact | Phosphor bronze | Au |
| Ferrule | Annealed Copper | Ni |
| Gasket(O-ring) | Silicone Rubber | － |
| Environmental |  |
| Operating Temperature Range | -40℃～+85℃ |
| RoHs | Compliant |  |